## Slide 1: A Biaxial Tissue Stretcher
Client: Frank Yin, MD. Ph.D
Group 30
Joshua Leibowitz
Krista Vedvik
Christopher Zarins

## Slide 2: Background
Cells in the body experience mechanical forces
  Heart
  Lungs
  Blood vessels
Laboratory cell cultures should recreate physiological conditions so the cell’s physiological responses can be studied

## Slide 3: Need for a Biaxial Cell Stretcher
Studying the effects of mechanical force on aortic endothelial cells
Orientation and organization of cells depends on exact stretching qualities
Controlling deformation in both directions gives the most accurate and meaningful results

## Slide 4: Design Requirements
Parameter | Value
Maximum Strain | 40%
Strain Resolution | 0.50%
Maximum Strain Rate | 40% / s
Maximum Operating Frequency | 2 Hz
Device Size | 50 cm W x 50 cm D x 60 cm H
Operating Temperature | 37.5 ˚ C
Operating Humidity | 100%
Substrate Stiffness | 100 kPa
Culture Size | 5 cm x 5 cm
Cost | < $35,000

## Slide 5: Overview of Design Alternatives
Superstructure
Drive Mechanism
Membrane Fixation

## Slide 6: Superstructure
Single Lever Arms
Parallelogram Linkage
Fixed Linear Rail
Sliding Linear Rail

## Slide 7: Superstructure: Mechanical Linkage
Single Lever Arm
Parallelogram Arm

## Slide 8: Superstructure: Linear Rails
Fixed Linear Rail
Sliding Linear Rail

## Slide 9: Superstructure Pugh Analysis
Superstructure |  |  |  |  | 
 | Weight | Sliding Linear Rail | Fixed Linear Rail | Single Lever Arm | Parallelogram Linkage
Precision | 8 | 7 | 8 | 7 | 6
Minimizing Fluid Shear | 7 | 8 | 8 | 1 | 3
Ease of Calibration | 6 | 10 | 10 | 2 | 4
Cost | 6 | 8 | 7 | 4 | 3
Ease of setup | 6 | 8 | 8 | 4 | 6
Optical Accessibility | 6 | 10 | 3 | 10 | 10
Multiple Membrane Capabilities | 4 | 9 | 10 | 1 | 6
Total |  | 364 | 328 | 187 | 231

## Slide 10: Drive Mechanism
Motor with Cam Drive
Stepper Motor with Rack Drive
Stepper Motor with Worm Drive
Stepper Motor with Lever Arms
Linear Actuator with Direct Fixation

## Slide 11: Drive Mechanism – Cam Drive

## Slide 12: Drive Mechanism
Linear Actuator
Stepper Motor with Worm Drive
Stepper Motor with Rack Drive

## Slide 13: Drive Mechanism Pugh Analysis
Drive Mechanism |  |  |  |  |  | 
 | Weight | Linear Actuator w/ Direct Fixation | Stepper Motor w/ Worm Gear | Stepper Motor w/ Rack Drive | Stepper Motor w/ Lever Arms | Motor w/ Cam Drive
Drive Precision | 9 | 10 | 8 | 4 | 5 | 2
Speed | 8 | 9 | 9 | 10 | 10 | 10
Cost | 8 | 1 | 8 | 8 | 9 | 10
Calibration | 7 | 10 | 7 | 8 | 5 | 1
Ease of setup | 6 | 10 | 9 | 9 | 9 | 2
Durability | 5 | 8 | 8 | 9 | 8 | 6
Total |  | 340 | 351 | 335 | 326 | 227

## Slide 14: Membrane Fixation
Fixation Strategy
  Sutures
  Clamps
Desirable Qualities
  Region of uniform strain
  Ease of setup

## Slide 15: Finite Element Analysis
Clamp Fixation
Suture Fixation

## Slide 16: Our Chosen Design

## Slide 17: Design Schedule
Task/Milestone | Nov. |  |  |  | Dec. | 
 | 5 | 12 | 19 | 26 | 3 | 10
Parts Research |  |  |  |  |  | 
Conceptualization of Final Design |  |  |  |  |  | 
Fluid Shear Finite Element Simulations |  |  |  |  |  | 
CAD Renditions |  |  |  |  |  | 
Risk Analysis & DesignSafe |  |  |  |  |  | 
Website Finalization |  |  |  |  |  | 
Feasibility Report |  |  |  |  |  | 
Final Oral Report |  |  |  |  |  | 
Final Written Report |  |  |  |  |  | 
Project Poster Judging |  |  |  |  |  | 

## Slide 18: Member Responsibilities
 | Chris | Josh | Krista
Conceptualization |  |  | 
 | x | x | x
Device Components |  |  | 
Substrate | x |  | 
Drive Mechanism |  |  | x
Controller Interface | x |  | 
Incubator Compatibility |  |  | x
Imaging Compatibility |  | x | 
Calibration |  | x | 
Risk Analysis |  |  | 
DesignSafe |  | x | 
Research |  |  | 
Feasibility | x | x | x
Literature Searches |  | x | 
Mathematical Parameters | x |  | 
Prices/Quotes |  |  | x
Final Report |  |  | 
Initializing |  | x | 
Scheduling/Labor Division |  |  | x
Figures |  |  | x
Copy-editing | x |  | 
Final Presentation |  |  | 
 |  |  | x
Final Poster |  |  | 
 | x | x | x
Client Interactions |  |  | 
 | x |  | x
Intellectual Property |  |  | 
 |  |  | x
Website |  |  | 
 |  | x | 

## Slide 19: References
Balland, M., et. al. Power Laws in Microrheology Experiments on Living Cells: Comparative Analysis and Modeling. Phys. Rev. E Stat. Nonlinear Soft Matter Phys. 74, (2006)
Collinsworth, A. et. al. Apparent Elastic Modulus and Hysteresis of Skeletal Muscle Cells Throughout Differentiation. Am. J. Cell Physiol. 283, C1219-C1227 (2002)
McGarry, J. et. al. A Comparison of Strain and Fluid Shear Stress in Stimulating Bone Cell Responses- A Computational and Experimental Study. FASEB J. 19, 482-484 (2005)
Thompson, M. et. al. Quantification and Significance of Fluid Shear Stress Field in Biaxial Cell Stretching Device. Biomech. Model Mechanobiol. 10, 559-564 (2011)
Yin, F., Chew, P., Zeger, S. An Approach to Quantification of Biaxial Tissue Stress-Strain Data. J. Biomech. 19, 27-37 (1986)
Zeng, D. et. al. Young’s Modulus of Elasticity of Schlemm’s Canal Endothelial Cells. Biomech. Model Mechanobiol. 9, 19-33 (2010)

## Slide 20: Questions?